## Slide 1
K J Somaiya College of Engineering, Mumbai-77
(Constituent college of Somaiya Vidyavihar University)
Operational Amplifiers
Presented by:
Prof. S A Hanumante

## Slide 2: Operational Amplifiers

## Slide 3: Outline of Presentation
What is an Op-Amp?
Characteristics of Ideal and Real Op-Amps
Common Op-Amp Circuits
Applications of Op-Amps
References

## Slide 4: What is an Op-Amp?
An Operational Amplifier (known as an “Op-Amp”) is a device that is used to amplify a signal using an external power source
Op-Amps are generally composed of:
Transistors, Resistors, Capacitors
= + +

## Slide 5
Leading to the advent of the modern IC which is still used even today (1967 – present)
Fairchild μA741
Electrical Schematic of μA741

## Slide 6: Op-Amps and their Math
A traditional Op-Amp:
: non-inverting input
: inverting input
: output
: positive power supply
: negative power supply
V+
V-
Vout
Vs+
Vs-
The difference between the two inputs voltages (V+ and V-) multiplied by the gain (K, “amplification factor”) of the Op-Amp gives you the output voltage
The output voltage can only be as high as the difference between the power supply (Vs+ / Vs-)and ground (0 Volts)
Vout = K (V+ - V-)

## Slide 7: Saturation
Saturation is caused by increasing/decreasing the input voltage to cause the output voltage to equal the power supply’s voltage*
The slope is normally much steeper than it is shown here. Potentially just a few milli-volts (mV) of change in the difference between V+ and V- could cause the op-amp to reach the saturation level
* Note that saturation level of traditional Op-Amp is 80% of supply voltage with exception of CMOS op-amp which has a saturation at the power supply’s voltage

## Slide 8: Outline of Presentation
What is an Op-Amp?
Characteristics of Ideal and Real Op-Amps
Common Op-Amp Circuits
Applications of Op-Amps
References

## Slide 9: An Ideal Op-Amp Characteristics
Infinite voltage gain
Infinite input impedance
Zero output impedance
Infinite bandwidth
Zero input offset voltage (i.e., exactly zero out if zero in).

## Slide 10: Ideal versus Real Op-Amps
Parameter | Ideal Op-Amp | Real Op-Amp
Differential Voltage Gain | ∞ | 105 - 109
Gain Bandwidth Product (Hz) | ∞ | 1-20 MHz
Input Resistance (R) | ∞ | 106 - 1012 Ω
Output Resistance (R) | 0 | 100 - 1000 Ω
Ideal
Real

## Slide 11: Outline of Presentation
What is an Op-Amp?
Characteristics of Ideal and Real Op-Amps
Common Op-Amp Circuits
Applications of Op-Amps
References

## Slide 12: Basic Op-Amp Circuits
An op-amp amplifies the difference of the inputs V+ and V- (known as the differential input voltage)
This is the equation for an open loop gain amplifier:
K is typically very large – at around 10,000 or more for IC Op-Amps
This equation is the basis for all the types of amps we will be discussing
Vout = K(V+-V-)

## Slide 13: Open Loop vs Closed Loop Circuit
A closed loop op-amp has feedback from the output to the input, an open loop op-amp does not
Open Loop
Closed Loop

## Slide 14: Op-Amp as Non-Inverting Amplifier
Amplifies the input voltage by a constant
Closed loop op-amp
Voltage input connected to non-inverting input
Voltage output connected to inverting input through a feedback resistor
Inverting input is also connected to ground
Non-inverting input is only determined by voltage output

## Slide 15: Op-Amp as Non-Inverting Amplifier
But , so
)
)

## Slide 16: Op-Amp as Inverting Amplifier
Amplifies and inverts the input voltage
Closed loop op-amp
Non-inverting input is determined by both voltage input and output
The polarity of the output voltage is opposite to that of the input voltage
Input Voltage is connected to inverting terminal
Output Voltage is fedback to inverting input through a feedback resistor
Non-inverting input is grounded

## Slide 17: Op-Amp as Inverting Amplifier
Apply KCL at inverting node of OPAMP
)

## Slide 18: Op-Amp as Adder/Summing Amplifier

## Slide 19: Op-Amp as Subtractor
If all resistors are equal:

## Slide 20: References
Op-amps and Linear Integrated Circuits
By Ramakant A Gaikwad
Publication: Pearson Education
Linear Integrated Circuits
By Choudhary D. Roy & Shail B. Jain
Publication: New Age International

## Slide 21
Thank you